## Slide 1: Simplification of Boolean Functions

## Slide 2: Simplification of Boolean Functions
An implementation of a Boolean Function requires the use of logic gates.
A smaller number of gates, with each gate (other then Inverter) having less number of inputs, may reduce the cost of the implementation.
There are 2 methods for simplification of Boolean functions.

## Slide 3: Simplification of Boolean Functions
The algebraic method by
  using Identities
The graphical method by
  using Karnaugh Map method
The K-map method is easy and straightforward.
A K-map for a function of n variables
  consists of 2n cells, and,
  in every row and column, two adjacent cells should differ in the value of only one of the logic variables.

## Slide 4: Karnaugh Map
Diagram made up of squares.
Each square represents one minterm.
A Boolean function is expressed in the map as the area enclosed by the squares whose minterms are included in the function.
The map presents a visual diagram of all possible ways a function may be expressed in standard form.

## Slide 5: Two-Variable Map
 | y |  | 
x |  | 0 | 1
 | 0 | mo (x’y’) | m1 (x’y)
 | 1 | m2 (xy’) | m3 (xy)
xy'
xy

## Slide 6: Two-Variable Map
 | y |  | 
x |  | 0 | 1
 | 0 | mo | m1
 | 1 | m2 | m3
F(x,y) = x + y = x’y + xy’ + xy = m1 + m2 + m3

## Slide 7: Two-Variable Map
 | y |  | 
x |  | 0 | 1
 | 0 |  | 1
 | 1 | 1 | 1
F(x,y) = x + y = x’y + xy’ + xy = m1 + m2 + m3

## Slide 8: Three-Variable Map
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6

## Slide 9: Three-Variable Map
 | y | z |  |  | 
x |  | 00 | 01 | 11 | 10
 | 0 | x’y’z’ | x’y’z | x’yz | x’yz’
 | 1 | xy’z’ | xy'z | xyz | xyz’

## Slide 10: Four-Variable Map
wx yz | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | M11 | m10

## Slide 11: Simplification Using the Map
Principle 1. “The more, the merrier.” Hence, a quad is better than a pair.
Principle 2. Share group elements only when necessary to form another or bigger group.

## Slide 12: Example 1
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 | 1 | 1 |  | 
The function F(x,y,z)=x’yz+x’yz’+xy’z’+xy’z
is mapped as follows:
The groups are:
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 | 1 | 1 |  | 

## Slide 13: Example 1
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 | 1 | 1 |  | 
The first group is read as x’y because these
are the variables unchanged:
The second group is read as xy’:
 | 00 | 01 | 11 | 10
0 |  |  |  | 
1 | 1 | 1 |  | 

## Slide 14: Example 1
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 | 1 | 1 |  | 
The simplified expression therefore is
f(x,y,z)=x’y+xy’

## Slide 15: Example 2
The function f(x,y,z)=x’yz+xy’z’+xyz+xyz’
is mapped as
 | 00 | 01 | 11 | 10
0 |  |  | 1 | 
1 | 1 |  | 1 | 1
The simplified expression is
f(x,y,z)=yz+xz’

## Slide 16: Example 3
The function f(A,B,C)=A’C+A’B+AB’C+BC
is mapped as
 | 00 | 01 | 11 | 10
0 |  | 1 | 1 | 1
1 |  | 1 | 1 | 
The simplified expression is
f(A,B,C)=C+A’B

## Slide 17: Example 4
The function f(x,y,z)=Σ(0,2,4,5,6)
is mapped as
 | 00 | 01 | 11 | 10
0 | 1 |  |  | 1
1 | 1 | 1 |  | 1
The simplified expression is
f(x,y,z)=z’+xy’

## Slide 18: Example 5
The function
f(w,x,y,z)=Σ(0,1,2,4,5,6,8,9,12,13,14)
is mapped as
 | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10
The simplified function is
f(w,x,y,z)=y’+w’z’+xz’

## Slide 19: Example 6
The function
f(A,B,C,D)=A’B’C’+B’CD’+A’BCD’+AB’C’
is mapped as
 | 00 | 01 | 11 | 10
00 | 1 | 1 |  | 1
01 |  |  |  | 1
11 |  |  |  | 
10 | 1 | 1 |  | 1
The simplified function is
f(A,B,C,D)=B’D’+B’C’+A’CD’

## Slide 20: The Relationship Between the Number of Adjacent Squares and the Number of Literals in a Term
 | No. of Adj. Sq. | Number of Literals in a Term in an n-variable Map |  |  |  |  | 
k | 2k | n=2 | n=3 | n=4 | n=5 | n=6 | n=7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 2 | 1 | 2 | 3 | 4 | 5 | 6
2 | 4 | 0 | 1 | 2 | 3 | 4 | 5
3 | 8 |  | 0 | 1 | 2 | 3 | 4
4 | 16 |  |  | 0 | 1 | 2 | 3
5 | 32 |  |  |  | 0 | 1 | 2
6 | 64 |  |  |  |  | 0 | 1

## Slide 21: Product of Sums Simplification
The minimized Boolean function derived from a k-map is expressed in the sum of products form.
The squares marked with 1’s in the map represent the minterms of the function.
The unmarked squares represent the complement of the function.

## Slide 22: Product of Sums Simplification
From the unmarked squares, we can obtain the simplified complement of the function.
Applying DeMorgan’s theorem on the simplified complement of the function, we obtain the simplified function in product of terms.

## Slide 23: Example
 | 00 | 01 | 11 | 10
00 | 1 | 1 |  | 1
01 |  | 1 |  | 
11 |  |  |  | 
10 | 1 | 1 |  | 1
Simplify the function
f(A,B,C,D)=Σ(0,1,2,5,8,9,10) in sum
of products and product of sums.

## Slide 24: Example
The simplified expression in
sum of products is given by
f(A,B,C,D)=B’D’+B’C’+A’C’D

## Slide 25: Example
 | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 1
01 | 0 | 1 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 1 | 0 | 1
The complement of the function is mapped as those marked with 0’s
as shown below:

## Slide 26: Example
 | 00 | 01 | 11 | 10
00 |  |  | 0 | 
01 | 0 |  | 0 | 0
11 | 0 | 0 | 0 | 0
10 |  |  | 0 | 
The simplified expression for the
complement of the function is
f‘(A,B,C,D)=AB+CD+BD’

## Slide 27: Example
The simplified expression for the
complement of the function is
f‘(A,B,C,D)=AB+CD+BD’
Applying DeMorgan’s theorem, we obtain the simplified function in product of sums:
f(A,B,C,D)=(A’+B’)(C’+D’)(B’+D)

## Slide 28: The Universal Gate
NAND
NOR
Universal gate because they can be used to implement any logic gate.

## Slide 29: Graphic Symbols for NAND
AND-Invert
F = (xyz)’
Invert-OR
F = x’+y’+z’

## Slide 30: Graphic Symbols for NOR
OR-Invert
F = (x+y+z)’
Invert-AND
F = x’y’z’

## Slide 31: Graphic Symbols for NOT
AND-Invert
OR-Invert
Buffer-Invert

## Slide 32: 2-Level NAND Implementation
Simplify the function and express it in sum of products.
Draw a NAND gate for each product term of the function that has at least two literals. The inputs to each NAND gate are the literals of the term. This constitutes a group of first-level gates.

## Slide 33: 2-Level NAND Implementation
Draw a single NAND gate (using the AND-invert or invert-OR graphic symbol) in the second level, with inputs coming from outputs of first-level gates.
A term with a single literal requires an inverter in the first level or may be complemented and applied as an input to the second-level NAND gate.

## Slide 34: 2-Level NOR Implementation
The NOR function is the dual of the NAND function.
Hence, all procedures and rules for NOR logic are the dual of the corresponding procedures and rules developed for the NAND logic.

## Slide 35: Rules for NAND / NOR Implementation
Case | Function to Simplify | Standard Form to Use | How to Derive | Implement with | Levels
A | F | Σ | Combine 1’s | NAND | 2
B | F’ | Σ | Combine 0’s | NAND | 3
C | F | π | Complement F’B | NOR | 2
D | F’ | π | Complement FA | NOR | 3

## Slide 36: Non-degenerate Forms
Consider 4 types of gates: AND, OR, NAND and NOR.
There are 16 different configurations of 2-level implementation.
8 are said to be degenerate forms because they degenerate to a single operation.
8 are non-degenerate forms because they produce an implementation in sum of products or product of sums.

## Slide 37: Non-degenerate Forms
AND-OR  | OR-AND 
NAND-NAND  | NOR-NOR 
NOR-OR | NAND-AND
OR-NAND | AND-NOR

## Slide 38: AND-OR-Invert
AND-NOR
NAND-AND

## Slide 39: OR-AND-Invert
AND-NOR
NAND-AND

## Slide 40: Rules for Other 2-Level Implementation
Equivalent Non-Degenerate Form |  | Implements the function | Simplify F’ in | To get an output of
AND-NOR | NAND-AND | AND-OR-Invert | Sum of products by combining 0’s in the map | F
OR-NAND | NOR-OR | OR-AND-Invert | Product of sums by combining 1’s in the map and then complementing | F
NAND-AND and NOR-OR requires a single-input inverter for a single literal term.

## Slide 41: DON’T-CARE Conditions
There are instances when not all the possible combinations of the inputs are used.
Example: BCD uses 4 bits, but there are 6 unused bit combinations.
We don’t care what the output for these unused input combinations is.
In a map, mark don’t-care with an ‘X’.

## Slide 42: Example
Simplify the Boolean function F(w,x,y,z)=Σ(1,3,7,11,15) and the don’t-care conditions d(w,x,y,z)=Σ(0,2,5)
 | 00 | 01 | 11 | 10
00 | X | 1 | 1 | X
01 |  | X | 1 | 
11 |  |  | 1 | 
10 |  |  | 1 | 

## Slide 43: Tabulation Method
The map method is convenient for 3- or 4-variable expressions.
As the number of variables increases, the excessive number of squares prevents a reasonable selection of adjacent squares.
Quine-McCluskey or Tabulation Method

## Slide 44: Tabulation Method
By an exhaustive search, find all the terms (called prime implicants) that are candidates for inclusion in the simplified function.
Choose among the prime implicants those that give an expression with the least number of literals.

## Slide 45: Finding Prime Implicants
Group binary representation of the minterms according to the number of 1’s contained.
Any 2 minterms which differ from each other by only one variable can be combined, and the unmatched variable removed.
This process is repeated as long as proper matching is encountered.

## Slide 46: Finding Prime Implicants
The unchecked terms in the table form the prime implicants.
A prime implicant table is used to select the prime implicants that form the minimized function.

## Slide 47: Example
Simplify F=Σ(0,1,2,8,10,11,14,15)
 | (a) |  |  |  | (b) |  |  |  | 
 | wxyz |  |  |  | wxyz |  |  |  | wxyz
0 | 0000 |  |  | 0,1 | 000– |  |  | 0,2,8,10 | –0–0
1 | 0001 |  |  | 0,2 | 00–0 |  |  | 0,8,2,10 | –0–0
2 | 0010 |  |  | 0,8 | –000 |  |  | 10,11,14,15 | 1–1–
8 | 1000 |  |  | 2,10 | –010 |  |  | 10,14,11,15 | 1–1–
10 | 1010 |  |  | 8,10 | 10–0 |  |  |  | 
11 | 1011 |  |  | 10,11 | 101– |  |  |  | 
14 | 1110 |  |  | 10,14 | 1–10 |  |  | F=w’x’y’+x’z’+wy | 
15 | 1111 |  |  | 11,15 | 1–11 |  |  |  | 
 |  |  |  | 14,15 | 111– |  |  |  | 

## Slide 48: Selection of Prime Implicants
 |  |  | 1 | 4 | 6 | 7 | 8 | 9 | 10 | 11 | 15
 | x’y’z | 1,9 | x |  |  |  |  | x |  |  | 
 | w’xz’ | 4,6 |  | x | x |  |  |  |  |  | 
 | w‘xy | 6,7 |  |  | x | x |  |  |  |  | 
 | xyz | 7,15 |  |  |  | x |  |  |  |  | x
 | wyz | 11,15 |  |  |  |  |  |  |  | x | x
 | wx’ | 8,9,10,11 |  |  |  |  | x | x | x | X | 
 |  |  |  |  |  |  |  |  |  |  |